## Slide 1
From Data to Decisions Under Uncertainty
ME 323 Module 1 — Lecture 2
A model that learns from sparse data and tells you how much it does not know. Flow and examples adapted from Prof. Bilionis's data-science lecturebook.

## Slide 2
Where Pre-lab 1 left you
  • You coded three capacity branches — flexural yield, junction shear-flow separation, LTB — calibrated (sigma_y, k, tau_i), and took the minimum: one capacity number per design.
  • The parity plot showed where that number holds and where it misses.
  • Your optimizer picked b = 1.10, H_web = 13.25 mm: predicted 48.7 N/g. Staff queried the oracle — a frozen model fit to a prior campaign of real bend tests, standing in for the testing machine — and it returned 482.6 N = 38.02 N/g on the estimated-mass basis. There all three mode capacities tie within ~1%, so the 'LTB' proxy is a knife-edge call.
The physics gave you a point estimate sitting exactly on a mode boundary — the region you trust it least. The missing ingredient is a statement of confidence.

## Slide 3
You already have most of this
From ME 239:
  • Bayes' rule, Gaussian distribution
  • Multivariate Gaussian and covariance
  • Conditioning a Gaussian on data
New today, but only one step past 239:
  • Gaussian Process; acquisition functions (Bayesian optimization)

## Slide 4
Bayes, in one line
You start with a belief about beam strength. You test a beam. You update the belief.
Carry a distribution over the unknown strength surface, not a single guess.
Every slide that follows is this line, applied to beams.

## Slide 5
A Gaussian is a belief about one beam
Where does 3% come from? Four repeat prints at (1.3, 12.8) spanned 548.6-566.1 N; pooled over all repeats the scatter runs ~4.4% with session/printer structure. 3% is the stated class working value.

## Slide 6
Two beams at once: covariance
Nearby designs share material, geometry, and physics, so their strengths move together.
The covariance matrix writes that down. This is the piece the GP is built on.

## Slide 7
Conditioning: measure one, update the other
Measure beam A and the joint Gaussian conditions: belief about B shifts and tightens.
You did this algebra in ME 239. Everything today is this move, repeated. (animated in slideshow)

## Slide 8
A function is a long Gaussian vector
Strength at 2 designs is a 2D Gaussian; at 120 designs, a 120-D Gaussian. Connect the dots and it is a function.
A kernel fills in the covariances: nearby beams correlate, distant ones do not. (animated in slideshow)

## Slide 9
A Gaussian Process, before and after data
Before data the kernel proposes candidate curves; each test kills the ones that disagree.
The module models log(str/w): exp(mu_log) is the posterior median in N/g; the band is conditional uncertainty.

## Slide 10
Watch it learn, one beam at a time
The band collapses where beams land and stays wide where nothing has been tested.
Earlier span-200 campaign; rebuilt from the new 44-beam dataset when testing finishes. (animated in slideshow)

## Slide 11
The kernel is a modeling choice
The length scale answers: how far does one test's influence reach?
No single right answer; there are defensible and indefensible ones.

## Slide 12
So is the noise
We assume 3% as the class working value. Pre-lab 2 refits at 1%, 3%, and 10%.
The recommendation does not move: 1%, 3%, and 10% all pick (1.00, 13.39) — the untested thin-b strip the widened box opened. Sensitivity evidence, not proof of the noise value.

## Slide 13
Epistemic and aleatory uncertainty do different jobs
  • Epistemic: uncertainty about the latent surface because tests are sparse. Informative beams can reduce it.
  • Aleatory: print-to-print and test-to-test scatter at one nominal design. Another location does not remove it.
  • For one future observation in log space: sigma_total = sqrt(sigma_epi^2 + r^2), with r = 0.03.
MUI and EI use epistemic sigma because they value learnable uncertainty. A reliability bound for one future printed beam uses total sigma.

## Slide 14
Explore vs exploit
Exploit: test where the posterior median is highest. Explore: test where epistemic uncertainty is widest. MUI (maximum upper interval) uses latent log space.

## Slide 15
The loop: Bayesian optimization
Fit, pick the acquisition argmax, test, refit. It probes the thin-web corner once, learns the dip, settles on the peak.
Seven tests, no gradient, no formula for the dip. (animated in slideshow)

## Slide 16
Expected Improvement, the other dial
EI asks: by how much would a new test beat the best beam so far, on average?
  • accounts for both latent mean mu and epistemic uncertainty sigma, like MUI,
  • but weighs improvement, so it stops caring about regions that cannot win,
  • and it has its own dial, xi: an improvement threshold. xi = 0 lets the probabilities trade on their own; larger xi counts only wins that clear the incumbent by that margin, pushing exploration.
MUI and EI can point at different next beams. The choice encodes your appetite for risk; Pre-lab 2 has you code both.

## Slide 17
Zoom out: spending a test budget
Each print-and-test costs a machine slot, a test engineer hour, and days of queue. The class gets two oracle queries — answered by the frozen staff model, cheap because the prior campaign already paid for that information — and each group gets one real print.
Optimal experimental design is the batch version of the acquisition question: given N tests, which set teaches the most or finds the best fastest?
Choosing the next test is the engineering decision.

## Slide 18
Physics-informed GP: the two tracks meet
Plain GP sees only (b, H_web). Submission 1 lane C also sees log(P_phys) and P_LTB/P_bend from the calibrated three-branch capacity.
Features sharpen the fit where their physics is useful; the separation branch carries one calibrated tau_i for an interface strength that scatters between sessions. (animated in slideshow)

## Slide 19
Two decisions are yours; the rest are stress tests
You will meet six modeling "knobs" in Submission 1. Do not treat them as six equal choices.
  • You own two decisions: the lane — how physics and data combine into one model — and the risk posture — how hard to chase predicted performance versus uncertainty.
  • The rest — kernel, noise, target scale — are stress tests. After you pick coordinates, swap the kernel and refit at 1% / 3% / 10% noise, and see whether your pick survives.
The strong conclusion is not "we chose RBF and 3%." It is: "our exact optimum moves under reasonable assumptions, but every defensible model points at this neighborhood" — or, just as strong: "the recommendation is unstable, so we bought information instead of chasing the current maximum."

## Slide 20
The decision map: put both models on the same axes
Calibrated physics (with mode boundaries), GP posterior median, their disagreement, and epistemic sigma — tested beams on every panel. Submission 1 builds this with your knobs.

## Slide 21
The activity from here
  • Pre-lab 2: fit the GP, write MUI (and EI), work the noise assumption, find the GP-recommended beam.
  • Two queries: the class equation design and the class GP design go to the oracle — the same two beams for everyone. Only two.
  • Submission 1: combine physics, GP, and the two new points; pick the beam you will print; defend it in the memo.
  • Print, test, reflect, redesign: Submission 2 folds your own test result back into the model and asks what it changes.

## Slide 22
Before next time: Pre-lab 2
In ME323_Module1_Prelab2_ML:
  • compare vanilla GP setups and read posterior median, epistemic uncertainty, and total predictive uncertainty,
  • write both MUI and EI,
  • refit under 1% / 3% / 10% noise and note what moves,
  • record the locked class design: b = 1.00 mm, H_web = 13.39 mm, posterior median 37.1 N/g.
That beam is the class's second oracle query. Bring your rationale, not just the number.